SIK Worksheets v.1.0	Name:
Circuit 2, High School	Date:

How is this circuit, or a circuit like it, used in everyday life? Provide at least three examples.
_________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Get your LEDs turned on? Great. Now you are going to add a dimmer switch to your LED on pin # 9.

What user interface component will you need to use as a dimmer? _Potentiometer, or soft pot_________ / Add the necessary text to the oneOnAtATime( ) / method for the code heavy way to add the dimmer. / (See next page) / There are two different way to add a dimmer without changing or adding code. Try to find one of these ways without destroying your LED. / Draw a schematic of your circuit in the the space to the right, adding your dimmer component so that it works. There are three different ways to do this. / What other component does the dimmer component in this circuit act as? / __Resistor_______________________________	Other options for schematics on next page.
The LED needs a PWM value that ranges from 0 – 255. The dimmer component gives you values from 0 – 1023. Write an equation below that will convert the value the dimmer component outputs to a LED friendly value. / __PWM = (dimmer/1024)* 256_______________ / The LED values 0 – 255 actually represent 256 different values. Why is that? / __Zero is the first value but is not counted in the number system.____________________________ / _________________________________________	Draw a logic flow chart of the LED with dimmer.

Imagine your LED circuit (without dimmer) as a meter indicating a sensor reading. Decide what kind of sensor you would like to use as an input and describe in your own words what would cause the meter to rise and fall. ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

int trimpotPin = 0;

void oneOnAtATime(){
  int delayTime = 100;
int sensorValue = map(analogRead(trimpotPin),0,1023,0,255)

  for(int i = 0; i <= 7; i++){
    int offLED = i - 1;
    if(i == 0) {
      offLED = 7;
    }
    analogWrite(ledPins[i], (sensorValue));
    digitalWrite(ledPins[offLED], LOW);
    delay(delayTime);
  }
}
or

int trimpotPin = 0;

void oneOnAtATime(){
  int delayTime = 100;

  for(int i = 0; i <= 7; i++){
    int offLED = i - 1;
    if(i == 0) {
      offLED = 7;
    }
    analogWrite(ledPins[i], (map(analogRead(trimpotPin),0,1023,0,255)));
    digitalWrite(ledPins[offLED], LOW);
    delay(delayTime);
  }
}