SIK Worksheets v.1.0	Name:
Circuit 4, Middle School	Date:

Ohm's Law: V = I * R I = V / R R = V / I

How is this circuit, or a circuit like it, used in everyday life? Provide at least three examples.
_________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Got your servo running? Great.

Give values for Voltage, Current and Resistance for the pin # 9 value while the servo is in motion. Find the current by breaking the circuit and measuring on signal wire. Find resistance using Ohm's Law. / Highest reading while Servo is in motion: / V = ___.4__v I = .03_mA R = 13333Ω / What does the Arduino pin # 9 do in this circuit? / _Provides the position to set the servo to. / Draw arrows to indicate direction of current on the dotted line. / Add an on/off switch to this schematic.
Draw a logic flow chart of the circuit here:	Draw one example of how this circuit could be used in everyday life. Label all components and give it a title.

A Servo can't rotate continuously more than 360 degrees, as opposed to a motor which can turn all the way past 360 degrees as many times as you like. However, a servo remembers what its position is while a motor only knows if it is running forward or backwards. Can you think of any situations in which you would need a Servo instead of a motor? How about the other way around? Write three examples, at least one of each, below.
_______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________