/*
SparkFun Inventor's Kit
Circuit03Expansion
Adapted from Oomlout's SIK Circuit 3
*/

//lines below assign PWM values for analogWrite on pin #9,
//UNCOMMENT LINES TO USE DIFFERENT VALUES FOR SPEED

// line below makes motor run 100%, comment it out
// and uncomment other lines to make motor run at different speeds
 int PWMvalue = 255;	//100% speed
// int PWMvalue = 63.75;	//25% speed
// int PWMvalue = 102; //40% speed
// int PWMvalue = 127;	//50% speed
// int PWMvalue = 153; //60% speed
// int PWMvalue = 191;	//75% speed

//if your motor doesn't run right away try giving it a little push

int motorPin = 9; // declare the pin the motor is connected to

// setup() - this function runs once when you turn your Arduino on
// set the motors pin to be an output

void setup()
{
 pinMode(motorPin, OUTPUT);
}

// loop() - this function will start after setup finishes and then repeat

void loop() // runs over and over again
{
analogWrite (9, PWMvalue);
//line above uses PWM (analogWrite) to make the motor run at whatever speed you set
}