/*
SparkFun Inventor's Kit
Circuit04Expansion
Adapted from:
 Sweep
 by BARRAGAN <http://barraganstudio.com>
and Circ-10: Temperature
by Oomlout
/*

#include <Servo.h>

Servo myservo; // create servo object to control a servo
        // a maximum of eight servo objects can be created

int temperaturePin = 0;

void setup()
{
  myservo.attach(9); // attaches the servo on pin 9 to the servo object
}

void loop(){

//getting the voltage reading from the temperature sensor
float temperature = getVoltage(temperaturePin);

//convert from 10 mv per degree with 500 mV offset to degrees (volts - 500mV)* 100
 temperature = (temperature - .5) * 100;

//map temp from -10F to 105F to a 0 to 180 value so servo will work as indicator
temperature = map (temperature, -24, 40, 0, 180);

    myservo.write(temperature); // tell servo to go to position in variable temp
    delay(15); // waits 15ms for the servo to reach the position

}
float getVoltage(int pin){
 return (analogRead(pin) * .004882814);
//converting from a 0 to 1024 digital range
// to 0 to 5 volts (each 1 reading equals ~ 5 millivolts
}