/*
SparkFun Inventor's Kit
Circuit10Expansion
Adapted from Oomlout's SIK Circuit 10
*/

int temperaturePin = 0;	// declare the pin the temp sensor is connected to

int LEDpin = 9;	// declare the pin the LED is connected to

// setup() - this function runs once when you turn your Arduino on

void setup()
{
  Serial.begin(9600);	// Start the serial connection with the computer
        // to view the result open the serial monitor
        // last button beneath the file bar (looks like a box with an antennae)
}

void loop() // loop runs over and over again while Arduino has power
{
 float temperature = getVoltage(temperaturePin);
// line above gets the voltage reading from the temperature sensor

 temperature = (temperature - .5) * 100;
// line above converts from 10 mV per degree with 500 mV offset to degrees in Celsius

int tempBright = map(temperature, 20, 30, 0, 255);
// maps temperature to an analogWrite (PWM) friendly value (0-255)
// you may have to change the above numbers 20 & 30 depending on how warm or cold it is.

 Serial.println(temperature); //prints the results to Serial

 analogWrite(LEDpin, tempBright);
// line above uses analogWrite to change brightness of LED to tempBright

 delay(1000); // waits 1 second
}

// getVoltage() - returns a voltage from the original digital temp sensor value

float getVoltage(int pin){
 return (analogRead(pin) * .004882814);
//line above converts from a 0 to 1024 digital range to 0 to 5 volts (each 1 digital equals ~ 5 millivolts)
}