/*
SparkFun Inventor's Kit
Circuit12Expansion
Note: This looks kinda complicated, but it's mostly just comments
 */

int lightPin = 0;	//photoresistor connected to analog pin 0

int trimPot = 1;	//trimpot connected to analog pin 1
int temperaturePin = 2;	//temp sensor connected to analog pin 2

int redPin = 3;	//red lead on RGB LED connected to digital (PWM) pin 3
int greenPin = 5;	//green lead on RGB LED connected to digital (PWM) pin 5
int bluePin = 6;	//blue lead on RGB LED connected to digital (PWM) pin 6

void setup(){	//runs once when Arduino starts up
  Serial.begin(9600);	//starts serial communication
  pinMode(redPin, OUTPUT);	//declares redPin as output
    pinMode(bluePin, OUTPUT);	//declares bluePin as output
      pinMode(greenPin, OUTPUT);	//declares greenPin as output
}

void loop(){	//loop runs over and over while Arduino has power

  int redValue = analogRead(lightPin);	//reads input from photoresistor

  redValue = map(redValue, 0, 1023, 0, 255);
//line above maps photoresistor value (too big) to LED friendly value

 analogWrite(redPin, redValue);
//line above uses PWM (analogWrite) to set the redPin to red LED value

 Serial.print(redValue);
  Serial.print(" ");
//two lines above use Serial to print out red LED value

   int blueValue = analogRead(trimPot);	//reads input from trimpot

     blueValue = map(blueValue, 0, 1023, 0, 255);
//line above maps trimpot value (too big) to LED friendly value

 analogWrite(bluePin, blueValue);
//line above uses PWM (analogWrite) to set bluePin to blue LED value

  Serial.print(blueValue);
    Serial.print(" ");
//two lines above use Serial to print out blue LED value

float temperature = getVoltage(temperaturePin);
//getting the voltage reading from the temperature sensor
temperature = (temperature – .5) * 100;
//converting from 10 mv per degree with 500 mV offset
            //to degrees ((volatge – 500mV) times 100)
temperature = map(temperature, -10, 43, 0, 255);

 analogWrite(greenPin, temperature);
//line above uses PWM (analogWrite) to set greenPin to temp value

  Serial.print(greenValue);
    Serial.print(" ");
//two lines above use Serial to print out blue LED value

  Serial.println ();	//println makes Serial communication start a new line

  delay(1000);	//waits so us slow humans can catch up
}

float getVoltage(int pin){
return (analogRead(pin) * .004882814); //converting from a 0 to 1023 digital range
                         // to 0 to 5 volts. each 1 reading equals ~ 5 millivolts