/*
SparkFun Inventor's Kit
Circuit03Expansion
Adapted from Oomlout's SIK Circuit 3
*/

//lines below assign PWM values for analogWrite on pin #9,
//UNCOMMENT LINES TO USE DIFFERENT VALUES FOR SPEED

// line below makes motor run 25%, comment it out
// and uncomment other lines to make motor run at different speeds
// troubles with the motor? Watch out for wires.
 int PWMvalue0 = 0; //0% speed
 int PWMvalue1 = 25.5; //10% speed
 int PWMvalue2 = 63.75;	//25% speed
 int PWMvalue3 = 85;	//33% speed
 int PWMvalue4 = 127;	//50% speed
 int PWMvalue5 = 170; //66% speed
 int PWMvalue6 = 191.25;	//75% speed
 int PWMvalue7 = 204;	//80% speed
 int PWMvalue8 = 229.5;	//90% speed
 int PWMvalue9 = 255;	//100% speed

int motorPin = 9; // declare the pin the motor is connected to

// setup() - this function runs once when you turn your Arduino on
// set the motors pin to be an output

void setup()
{
  Serial.begin(9600);
 pinMode(motorPin, OUTPUT);
}

// loop() - this function will start after setup finishes and then repeat

void loop() // runs over and over again with all the different
{	// PWM values
analogWrite (9, PWMvalue0);
Serial.println(PWMvalue0);
delay(3000);
analogWrite (9, PWMvalue1);
Serial.println(PWMvalue1);
delay(3000);
analogWrite (9, PWMvalue2);
Serial.println(PWMvalue2);
delay(3000);
analogWrite (9, PWMvalue3);
Serial.println(PWMvalue3);
delay(3000);
analogWrite (9, PWMvalue4);
Serial.println(PWMvalue4);
delay(3000);
analogWrite (9, PWMvalue5);
Serial.println(PWMvalue5);
delay(3000);
analogWrite (9, PWMvalue6);
Serial.println(PWMvalue6);
delay(3000);
analogWrite (9, PWMvalue7);
Serial.println(PWMvalue7);
delay(3000);
analogWrite (9, PWMvalue8);
Serial.println(PWMvalue8);
delay(3000);
analogWrite (9, PWMvalue9);
Serial.println(PWMvalue9);
delay(3000);
analogWrite (9, PWMvalue8);
Serial.println(PWMvalue8);
delay(3000);
analogWrite (9, PWMvalue7);
Serial.println(PWMvalue7);
delay(3000);
analogWrite (9, PWMvalue6);
Serial.println(PWMvalue6);
delay(3000);
analogWrite (9, PWMvalue5);
Serial.println(PWMvalue5);
delay(3000);
analogWrite (9, PWMvalue4);
Serial.println(PWMvalue4);
delay(3000);
analogWrite (9, PWMvalue3);
Serial.println(PWMvalue3);
delay(3000);
analogWrite (9, PWMvalue2);
Serial.println(PWMvalue2);
delay(3000);
analogWrite (9, PWMvalue1);
Serial.println(PWMvalue1);
delay(3000);
analogWrite (9, PWMvalue0);
Serial.println(PWMvalue0);
delay(3000);
}