/* ---------------------------------------------------------

 * | Experimentation Kit for Arduino Example Code |

 * | CIRC-14 .: Fancy Sensing :. (Soft Potentiometer) |

 * ---------------------------------------------------------

 *

 * Will fade an RGB LED from Red-Green-Blue in relation to the

 * soft pot value

 *

 */

// LED leads connected to PWM pins

const int RED_LED_PIN = 9; //Red LED Pin

const int GREEN_LED_PIN = 10; //Green LED Pin

const int BLUE_LED_PIN = 11; //Blue LED Pin

void setup() {

  //no need for any code here

}

void loop() {

  int sensorValue = analogRead(0); //read the Soft Pot

  int redValue = constrain(map(sensorValue, 0, 512, 255, 0),0,255); //calculate the red Value (255-0 over the range 0-512)

  int greenValue = constrain(map(sensorValue, 0, 512, 0, 255),0,255)-constrain(map(sensorValue, 512, 1023, 0, 255),0,255); //calculate the green value (0-255 over 0-512 & 255-0 over 512-1023)

  int blueValue = constrain(map(sensorValue, 512, 1023, 0, 255),0,255); //calculate the blue value 0-255 over 512-1023

  // Display the requested color

  analogWrite(RED_LED_PIN, redValue);

  analogWrite(GREEN_LED_PIN, greenValue);

  analogWrite(BLUE_LED_PIN, blueValue);

}